## Slide 1: An Introduction to C
Adam Gleitman
6.270 – IAP 2014

## Slide 2: What a C Program Looks Like
#include <joyos.h>
int usetup(void) {
return 0;
}
int umain(void) {
// Your code here...
return 0;
}
statements
comments
functions
preprocessor

## Slide 3: A More Interesting Program
int umain(void) {
// Turn motor 0 on
motor_set_vel(0, 200);
// Wait 3 seconds
pause(3000);
// Turn motor 0 off
motor_set_vel(0, 0);
return 0;
}

## Slide 4: The Obligatory “Hello World”
The printf function writes a particular string to the USB serial port of the HappyBoard.
To view the output on your computer:
Windows users: Termite or PuTTY
Mac/Linux users: $ screen <portname> <baudrate>
int umain(void) {
printf("Hello world!\n");
return 0;
}
'\n' denotes the end of a line

## Slide 5: Variables
int umain(void) {
uint8_t x = 12;
uint8_t y = 15;
uint8_t z = 19;
z = x + y;
x = 41;
x = x - 4;
y *= 7; // y = y * 7;
z++; // z += 1;
x = (y - 6) / (x - z);
return 0;
}
x
12
y
15
z
19
27
41
37
105
28
11

## Slide 6: Data Types
uint8_t x = 12;
This means that x is:
unsigned
an integer
8 bits wide
In other words:
0 ≤ x ≤ 28 – 1

## Slide 7: Data Types: Integers
Number of bits | Signed | Unsigned
8 | int8_t −27 ≤ x ≤ 27 − 1 −128 ≤ x ≤ 127 | uint8_t 0 ≤ x ≤ 28 − 1 0 ≤ x ≤ 255
16 | int16_t −215 ≤ x ≤ 215 − 1 −32,768 ≤ x ≤ 32,767 | uint16_t 0 ≤ x ≤ 216 − 1 0 ≤ x ≤ 65,535
32 | int32_t −231 ≤ x ≤ 231 − 1 −2.15 × 109 ≤ x ≤ 2.15 × 109 | uint32_t 0 ≤ x ≤ 232 − 1 0 ≤ x ≤ 4.3 × 109
64 | int64_t −263 ≤ x ≤ 263 − 1 −9.22 × 1018 ≤ x ≤ 9.22 × 1018 | uint64_t 0 ≤ x ≤ 264 − 1 0 ≤ x ≤ 18.4 × 1018

## Slide 8: Data Types: Real Numbers
float (32-bit)
−3.4 × 1038 ≤ x ≤ 3.4 × 1038
smallest positive value is approximately 1.18 × 10−38
always signed
around 7 significant figures of accuracy
For the compiler (avr-gcc) we’re using, double is the same as float
Examples:
float g = -9.80665;
float avogadro = 6.022e23;
float charge = 1.6e-19;

## Slide 9: Printing Values of Variables
32 plus 11 equals 43
32 minus 11 equals 21
int umain(void) {
uint8_t x = 32;
uint8_t y = 11;
uint8_t z = x + y;
printf("%d plus %d equals %d\n", x, y, z);
printf("%d minus %d equals %d\n", x, y, x-y);
return 0;
}
The special formatters, indicated by %d, are replaced by the values of these variables.

## Slide 10: Other printf Formatters
Formatter | Description of what will be printed
%d | A 16-bit integer
%03d | A 16-bit integer, padded with zeros to occupy 3 digits (e.g., 017)
%4d | A 16-bit integer, padded with spaces to occupy 4 characters
%u | A 16-bit unsigned integer
%f | A floating-point number with six digits of precision (the default)
%.3f | A floating-point number with three digits of precision
%x | A hexadecimal number
%ld | A 32-bit (signed) integer
%% | A percent sign (%) – this does not require an additional argument
A more detailed list of formatters can be found here:
http://www.nongnu.org/avr-libc/user-manual/group__avr__stdio.html#gaa3b98c0d17b35642c0f3e4649092b9f1

## Slide 11: Conditionals
Heading > 90°?
Left wheel forwards
Right wheel backwards
Left wheel backwards
Right wheel forwards
YES
NO

## Slide 12: Conditionals
if (heading > 90.0) {
left_wheel_vel = 75;
right_wheel_vel = -75;
} else {
left_wheel_vel = -75;
right_wheel_vel = 75;
}
motor_set_vel(0, left_wheel_vel);
motor_set_vel(1, right_wheel_vel);

## Slide 13: Conditionals
if (heading > 135.0) {
left_wheel_vel = 150;
right_wheel_vel = -150;
} else if (heading > 90.0) {
left_wheel_vel = 75;
right_wheel_vel = -75;
} else {
left_wheel_vel = -75;
right_wheel_vel = 75;
}
motor_set_vel(0, left_wheel_vel);
motor_set_vel(1, right_wheel_vel);
You can run multiple mutually exclusive tests by using else if.
You can have as many tests as you want.

## Slide 14: Conditionals
if (heading > 88.0 && heading < 92.0) {
printf("Close enough.");
}
Comparators: Boolean operators:
x == y equals x && y AND
x != y not equals x || y OR
x < y less than !x NOT
x > y greater than
x <= y less than or equal to
x >= y greater than or equal to
You don’t need to include an else statement if you don’t need it.

## Slide 15: Loops: while
General form:
while (<condition>) {
<actions>
}
Here’s a neat little trick:
while (1) { // loop forever
int i = frob_read_range(0, 100);
printf("The frob is at: %d\n", i);
pause(200);
}

## Slide 16: Loops: for
General form:
for (<initialization>; <condition>; <increment>) {
<actions>
}
This will print out the numbers from 1 through 10:
int n;
for (n = 1; n <= 10; n++) {
printf("%d\n", n);
}

## Slide 17: Example 1: Drive Straight
int usetup(void) {
gyro_init(11, 1400000L, 1000);
return 0;
}
int umain(void) {
while (1) {
float deg = gyro_get_degrees();
if (deg < 0) {
motor_set_vel(0, 40);
motor_set_vel(1, 90);
} else {
motor_set_vel(0, 90);
motor_set_vel(1, 40);
}
}
return 0;
}

## Slide 18: Example 2: Ball Dispenser
uint8_t last_bump = false;
while (1) {
uint8_t cur_bump = (analog_read(8) < 500);
if (cur_bump && !last_bump) {
servo_set_pos(0, 341);
pause(300);
servo_set_pos(0, 220);
pause(400);
}
last_bump = cur_bump;
}

## Slide 19: Making Your Own Functions
int umain(void) {
// ...
float d2, d;
d2 = (myX - mouseX) * (myX - mouseX) +
(myY - mouseY) * (myY - mouseY);
d = sqrt(d2);
if (d < 10.0) { // mouse within 10 cm?
// ...
}
// ...
}
This seems useful. Can we find a way to make this code more reusable?

## Slide 20: Making Your Own Functions
Now we can call point_near wherever we want without copying and pasting large blocks of code!
This must be placed above* any calls we make to it.
uint8_t point_near(float x1, float y1, float x2, float y2) {
float d2;
d2 = (x2-x1)*(x2-x1) + (y2-y1)*(y2-y1);
return sqrt(d2) < 10.0;
}
int umain(void) {
// ...
if (point_near(myX, myY, mouseX, mouseY)) {
// ...
}
// ...
}
return type
arguments

## Slide 21: Making Your Own Functions
void set_drive_speed(int16_t left, int16_t right) {
motor_set_vel(0, left);
motor_set_vel(1, -right);
}
void drive_forward() {
set_drive_speed(100, 100);
}
void stop(void) {
set_drive_speed(0, 0);
}
A function doesn’t have to return a value. In this case, the return type should be void.
A function doesn’t have to contain any arguments. In this case, place the word void in between the parentheses or don’t put anything there.
You would call these functions as drive_forward() and stop().

## Slide 22: Organizing Your Code Better
// Declare functions
uint8_t point_near(float, float, float, float);
int umain(void) {
// body of umain
}
uint8_t point_near(float x1, float y1,
float x2, float y2) {
// body of point_near
}
Alternative strategy:
Declare a function first, and define it later!

## Slide 23: Organizing Your Code Better
#include <joyos.h>
#include "point_near.h"
int usetup(void) {
// ...
}
int umain(void) {
// ...
}
#ifndef __POINT_NEAR_H__
#define __POINT_NEAR_H__
uint8_t point_near(
float, float,
float, float);
#endif
#include "point_near.h"
uint8_t point_near(
float x1,
float y1,
float x2,
float y2) {
// ...
}
umain.c
point_near.c
point_near.h
Define these new functions in this file.
Declare new functions in this header file.
To use these functions, #include the header file at the top and pass the corresponding C file into the compiler.

## Slide 24: The Makefile
# User source files
USERSRC = user/robot/umain.c user/robot/point_near.c
#AVRDUDE_PORT = /dev/tty.usbserial-0000113D
AVRDUDE_PORT ?= com7
#AVRDUDE_USERPORT = /dev/tty.usbserial-A20e1uZB
AVRDUDE_USERPORT ?= com7
CC = avr-gcc
MCU = atmega128
OBJCOPY = avr-objcopy
AVRDUDE = avrdude
FTDI_EEPROM = ftdi_eeprom
...

## Slide 25: Including Libraries
We have provided you with several libraries that may be useful for performing computations.
http://www.nongnu.org/avr-libc/user-manual/modules.html
For example, <math.h> contains sqrt, trig functions, mathematical constants, etc.
<stdlib.h> contains abs, random number generation, etc.
To include one of these libraries, put the following line at the top of your code with the appropriate library name:
#include <math.h>

## Slide 26: Defining Constants
You can also define constants like this:
#define SQRT_3 1.73205080757
#define GYRO_PIN 11
#define LEGO_STUD_WIDTH 0.8
#define LEGO_BRICK_HEIGHT (1.2 * LEGO_STUD_WIDTH)
#define LEGO_PLATE_HEIGHT (LEGO_STUD_WIDTH / 3.0)

## Slide 27: Common Mistakes
int x = 4;
if (x = 5) {
printf("WTF?!\n");
}
float a = 0.3;
float b = 0.4;
if (a + b != 0.7) {
printf("MATH FAIL!\n");
}
uint8_t n;
for (n = 0; n < 300; n++) {
printf("%d\n", n);
}
x = 5 assigns a new value; it does not check if x equals 5.
Instead, use x == 5.
Floating-point arithmetic is subject to rounding error. Instead, check if a + b and 0.7 differ by at most a fixed constant epsilon.
uint8_ts have a maximum value of 255. Incrementing n at this value will cause an overflow, and the value will reset to 0. This for loop will never terminate.

## Slide 28: Common Mistakes, Fixed
int x = 4;
if (x == 5) {
printf("WTF?!\n");
}
float a = 0.3;
float b = 0.4;
if (abs(a + b - 0.7) >= 1e-6) {
printf("MATH FAIL!\n");
}
uint16_t n;
for (n = 0; n < 300; n++) {
printf("%d\n", n);
}

## Slide 29: Another Common Mistake
int x = 5;
int y = 2;
if (abs(x / y - 2.5) >= 1e-6) {
printf("WRONG!\n");
}
if (abs((float) x / y - 2.5) < 1e-6) {
printf("Much better!\n");
}
When dividing two integers, the remainder is dropped. You need to explicitly cast one of the operands of the division to a float in order to get a decimal answer.

## Slide 30: Partial Function Reference
Function | Description
digital_read(pin) | Reads the input on a pin. Returns 0 or 1.
analog_read(pin) | Reads the analog voltage on a pin. Returns a number between 0 and 1023, which correspond to 0 V and 5 V respectively.
motor_set_vel(motor, vel) | Sets the velocity on the specified motor. vel ranges from −255 to 255.
motor_brake(motor) | “Brakes” the specified motor.
servo_set_pos(servo, pos) | Sets the specified servo to a specified position. pos ranges from 0 to 511.
servo_disable(servo) | Turns off control signals to a servo. This is useful for stopping continuous rotation servos.
frob_read_range(low, high) | Reads the frob knob. Returns an integer between low and high.
pause(millis) | Pauses the program for a certain number of milliseconds.

## Slide 31: Partial Function Reference
Function | Description
printf(str, params...) | Prints text to the USB port.
go_click() | Pause the program until the GO button is pressed.
stop_click() | Pause the program until the STOP button is pressed.
go_press() | Returns 1 if the GO button is pressed, 0 otherwise.
stop_press() | Returns 1 if the STOP button is pressed, 0 otherwise.
encoder_read(pin) | Returns the number of encoder clicks that have happened on a particular encoder since it was last reset.
encoder_reset(pin) | Resets the counter for the given encoder to 0.
get_time() | Returns the number of milliseconds that have passed since the HappyBoard was turned on.
get_time_us() | Returns the number of microseconds that have passed since the HappyBoard was turned on.